|  | FORM ACB-FA3 ACB FACILITY AND EQUIPMENT QUESTIONNAIRE FOR ACTIVE CHILLED BEAMS (ACB) |
| --- | --- |

Company (Participant) Name

Test Facility Address and Unique Name

- Facility information

| Facility Floor area | Test floor floor area | Indicate ft2 |  |
| --- | --- | --- | --- |
| Facility height | Dimension | Indicate x’-y” |  |
| Facility leakage | @ 0.2 in. H2O pressure | Indicate cfm/ft2 |  |
| Facility heat flow | Perimeter wall heat flow loss | Indicate Btu/h/ft2 |  |
| Heat supply method used | Internal or External or Both |  |

- Test Facility Limitations

| Operating Range of Facility | Min. Sensible Cooling Capacity | Indicate Btu/h |  |
| --- | --- | --- | --- |
|  | Max. Sensible Cooling Capacity |  |  |
| Water Flow | Minimum Capacity | Indicate gpm |  |
|  | Maximum Capacity |  |  |
| Airflow | Maximum Conditioning Equipment Airflow Capacity | Indicate cfm |  |
| Sound Level | Non-weighted sound power level | dB |  |
| Physical Size | Dimensions of largest unit you can place in your facility (indicate ft or m) | Length |  |
|  |  | Height |  |
|  |  | Width |  |

- Time Requirements

| How long does it take to install and fully instrument a unit for test? | # of Persons |  |
| --- | --- | --- |
|  | Total # of man-hours |  |
| How long does it take to conduct a standard rating test from start to finish, including calculations? | # of Persons |  |
|  | Total # of man-hours |  |
| How many shifts per day will you employ for witness testing? | Length of shift, hrs. |  |
|  | # of shifts |  |

- Water Temperature Measurement

| Instruments for determining water temperature | Instrument Accuracy | Frequency of calibration, months | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- |
| RTD |  |  | □ Yes □ No |
| Thermocouple |  |  | □ Yes □ No |
| Other: |  |  | □ Yes □ No |
| Data Acquisition Type |  |

- Where do you place your water temperature measuring instruments?: __________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- Air Temperature Measurement

| Instruments for determining air temperature | Instrument Accuracy | Frequency of calibration, months | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- |
| RTD |  |  | □ Yes □ No |
| Thermocouple |  |  | □ Yes □ No |
| Thermopile |  | N/A | □ Yes □ No |
| Other: |  |  | □ Yes □ No |
| Data Acquisition Type |  |

- Are thermocouples all made from the same spool of wire ? □ Yes   □ No □ N/A

- Is the room airflow at a constant rate or is it adjusted depending on the unit being tested? _________________________________________________________________

- For the largest size unit you will test, how many air changes will the facility be handling?

_________________________________________________________________

- Water Flow Measurement

| Flow measuring instruments used | Instrument Accuracy | Diameter | Frequency of calibration, months | To what code standard(s), if any, is the instrument installed? | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- | --- | --- |
| Rota meter |  |  |  |  | □ Yes □ No |
| Turbine meter |  |  |  |  | □ Yes □ No |
| Orifice meter |  |  |  |  | □ Yes □ No |
| Magnetic meter |  |  |  |  | □ Yes □ No |
| Other |  |  |  |  | □ Yes □ No |
| Data Acquisition Type |  |  |

- Is the flow measuring device installed according to the manufacturer’s specification?  □ Yes   □ No

- What is the length of straight pipe upstream of flow measuring device?      _____________(ft)

- What is the length of straight pipe downstream of flow measuring device?  _____________(ft)

- Water Pressure Drop Measurement

| Water Pressure Drop instruments used | Instrument Accuracy | Frequency of calibration, months | To what code standard(s), if any, is the instrument installed? | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- | --- |
| Differential Pressure |  |  |  | □ Yes □ No |
| Absolute pressure 1 |  |  |  | □ Yes □ No |
| Absolute pressure 2 |  |  |  | □ Yes □ No |
| Other |  |  |  | □ Yes □ No |
| Data Acquisition Type |  |

- Describe the location of static pressure taps: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- Barometric Pressure Measurement

| Barometric Pressure Drop instrument used | Instrument Accuracy | Frequency of calibration, months | To what code standard(s), if any, is the instrument installed? | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- | --- |
| Differential Pressure |  |  |  | □ Yes □ No |
| Absolute pressure 1 |  |  |  | □ Yes □ No |
| Other |  |  |  | □ Yes □ No |
| Data Acquisition Type |  |

- What is the approximate elevation above sea level of your test Facility?___________ (ft)

- What is the approximate standard barometric pressure at the location of your test Facility?_______ (psia)

- Sound Power Measurement

| Power measurement devices | Instrument Accuracy | Frequency of calibration, months | To what code standard(s), if any, is the instrument installed? | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- | --- |
|  |  |  |  | □ Yes □ No |
| Data Acquisition Type |  |

- Air Speed Measurement

| Air Speed measurement devices | Instrument Accuracy | Frequency of calibration, months | To what code standard(s), if any, is the instrument installed? | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- | --- |
| Anemometer |  |  |  | □ Yes □ No |
| Other |  |  |  |  |
| Data Acquisition Type |  |

- Discharge Air Jet Performance Measurement

| Discharge Air Jet Performance measurement devices | Instrument Accuracy | Frequency of calibration, months | To what code standard(s), if any, is the instrument installed? | Is the primary standard traceable to NIST or a comparable National Standard? |
| --- | --- | --- | --- | --- |
|  |  |  |  | □ Yes □ No |
| Data Acquisition Type |  |

- Data Acquisition

- Describe data acquisition system and data obtained (averaging or instantaneous):

________________________________	_________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- Facility Limitations

- Identify all Facility limitations for achieving AHRI test conditions (i.e. weather dependencies; air flow rates; etc):

________________________________	_________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

- Identify all limitations for conducting AHRI certification testing (i.e. Facility availability; operator training, etc): _______________________________________________________________________________

________________________________	_________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

Submitted By:

| Signature | Title |
| --- | --- |
| Printed Name | Date |